## Slide 1: Learning hand-eye co-ordination for robotic grasping
With Deep learning and large-scale data collection
Paper by : Sergey Levine, Peter Pastor, Alex Krizhevsky, Deirdre Quillen
Presentation by : Shivani Ghatge (spg2134)ION BY : SHIVANI GHATGE (spg2134)

## Slide 2: Outline
1. Introduction
2. Previous Related work
3. Deep Learning with Continuous Visual Input
4. Data Collection
5. Experiments
6. Interpretation as Reinforcement Learning

## Slide 3: Introduction
Human Hand Eye coordination - Hand-eye coordination, or eye-hand coordination, is the ability to do activities that require the simultaneous use of our hands and eyes.
Suggested approach –
  Data Driven and Goal Oriented
Main Contributions
  Learning continuous visual servoing for robot grasping
  CNN architecture for learning to predict the outcome of a grasp attempt
  Large scale data collection framework

## Slide 4: Related Work
Robotic Grasp –
  Geometric Methods -
    Force Closure (Weisz & Allen, 2012)
    Caging (Rodriguez et al., 2012).
  Data Driven methods –
    Human-supervised methods that predict grasp configurations (Herzog et al., 2014; Lenz et al., 2015)
    Methods that predict finger placement from geometric criteria computed offline (Goldfeder et al., 2009a)
Data Collection –
  Collecting datasets of object scans (Mahler et al., 2016), Oberlin & Tellex (2015)
  Collective robot learning and an instance of cloud robotics (Inaba et al., 2000; Kuffner, 2010;Kehoe et al., 2013; 2015).
Visual Servoing –
  Moving a camera or end-effector to a desired pose using visual feedback (Kragic & Christensen,2002)
Pinto and Gupta (2015)

## Slide 5: Procedure
This approach for Hand-Eye coordination for Robotic Grasping consists of two parts
  Prediction Network : This includes a CNN g(It , vt ) This accepts a visual input It and a task-space motion command vt , and outputs the predicted probability that executing the command will produce a successful grasp.
  Servoing function : A servoing function f(It ) that uses the prediction network to continuously control the robot to servo the gripper to a successful grasp.
  Data Collection :
    To train the prediction network, 800,000 grasp attempts were collected using a set of similar robotic Manipulators
    To ensure generalization of the learned prediction network, the specific parameters of each robot varied in terms of the camera pose relative to the robot providing independence to camera calibration

## Slide 7: Grasp Success Prediction with CNN
The grasp prediction network g(It , vt ) is trained to predict whether a given task-space motion will result in a successful grasp based on the current camera observation.
Requirements :
  Parse the current camera image
  Locate the gripper
  Determine whether moving the gripper according to vt will put it in a position where closing the fingers will pick up an object.
This is a complex spatial reasoning task that requires these abilities :
  Ability to parse the geometry of the scene
  Ability to interpret material properties and spatial relationships between objects which strongly affects the success of a given grasp.

## Slide 8: CNN - Data
Data for training CNN is obtained by attempting grasps using real physical robots.
Each grasp consists of T time steps .
At each time step the robot records the current image
and the current pose
The robot then chooses the direction along which to move the gripper.
At time step T, the robot closes the gripper and evaluates the success of the grasp producing label
Each grasp results in T samples denoted

## Slide 9: CNN - Architecture

## Slide 10: Continuous Servoing - Sampling
The servoing mechanism uses the grasp prediction network to choose the motor commands for the robot that will maximize the probability of a success grasp.
Perform inference in order to determine the motor command vt given an Image It
Approach 1 – Randomly sample a set of candidate motor commands vt and then evaluate g(It,vt)
Approach 2 – Optimization using Cross-Entropy Method
CEM – Derivative free optimization algorithm that samples a batch pf N values at each iteration, fits a Gaussian distribution to M<N of these samples and then samples a new batch of N from this distribution
N=64, M=6, 3 iterations

## Slide 11: Continuous Servoing - Algorithm
The predicted grasp success produced by the network can be used to inform a heuristic for raising and lowering the gripper, choose when to stop moving and attempt a grasp
Heuristic 1 – Close the gripper whenever the network predicts that where Ø means no motion, will succeed with at least 90% of the probability of success for
Heuristic 2 – Raise the gripper off the table when has a probability of success that is less than 50% of

## Slide 12: Data Collection
Parallelized data collection across up to 14 separate robots.
800,000 Grasp attempts over the course of 2 months without any manual annotation or supervision
Started with random motor command selection and T=2
For random motor commands 10%-30% success rate
Half of the dataset collected using random grasps and the rest used the latest network fitted for the data so far
Network updated 4 times, T increased from 2 to 10
Success of the grasp? 1cm between fingers and drop test

## Slide 13: Large Scale Data Collection

## Slide 14: Experiments

## Slide 15: Experiments
Questions –
Does continuous servoing significantly improve grasping accuracy and success rate?
How well does this approach perform compared to other approaches?
Open loop method
Random Baseline
Hand-Engineered grasping system

## Slide 16: Improved Grasp Success rate

## Slide 17: Reinforcement Learning?
Relationship between training the grasp prediction network and reinforcement learning
When T=2, only 1 decision is made by the servoing mechanism, the grasp network can be considered as an approximation of Q-function for the policy defined by the servoing mechanism f(It) and a reward function that is 1 when the grasp succeeds and 0 otherwise
Refitting grasp network – Q iteration
What happens when T>2 – Final probability of success from [I(t),p(t+1)-p(t)]
Assumption that actions induce a transitive relation between states
Combine with standard RL formulations that consider effects of intermediate actions
Enable the robot to perform nonprehensile manipulations to intentionally reorient and reposition objects prior to grasping

## Slide 18: Questions?